## Slide 1: PID controllers
Lecture 18

## Slide 2: What is a PID controller?
A proportional-integral-derivative controller (PID controller) is a control loop feedback mechanism (controller) widely used in process industry.
Continuous-time text book equation:
Proportional Action
Integral Action
Derivative Action
Note: 90% (or more) of control loops in industry are PID

## Slide 3: What is a PID controller?
A proportional action will have the effect of reducing the rise time and will reduce but never eliminate the steady-state error (unless the model of the plant has a pole at or ).
An integral action will have the effect of eliminating the steady-state error for a constant or step input, but it may make the transient response slower.
A derivative action will have the effect of increasing the stability of the system, reducing the overshoot, and improving the transient response. But it has the drawback of amplifying the noise present in the error signal.

## Slide 4: Analog and Digital formulations
Proportional Control
The discrete implementation of proportional control is identical to the continuous one. The continuous is
and the discrete is
where or is the error signal.

## Slide 5: Analog and Digital formulations
Derivative Control
The continuous-time Integral control is
The discrete-time derivative control is
where is the sampling time.

## Slide 6: Analog and Digital formulations
Integral Control
The continuous-time integral control is
The discrete-time integral control is
where is the sampling time.

## Slide 7: Analog and Digital formulations
Digital PID controller (conventional version)
where are the new integral and derivative gains
Digital PI controller
Digital PD controller

## Slide 8: Analog and Digital formulations
Digital PID controller (alternative version)
If we discretize the continuous-time (analog) PID controller using the bilinear transformation,
we obtain an alternative form for a digital PID controller
where , , and are design parameters.

## Slide 9: Analog and Digital formulations
https://www.youtube.com/watch?v=JEpWlTl95Tw
PID Math Demystified

## Slide 10: Analog Implementation
reverse
direct
Voltmeters
The key building block is the operational amplifier (op-amp).
PV – Process Variable
SP – Setpoint
Output – Control action
Manual Output Adjust

## Slide 11: Analog Implementation
FOXBORO 62H-4E-OH M/62H
Analog PID controller:

## Slide 12: Analog Implementation
Analog PI Motor Speed Control
https://www.youtube.com/watch?v=6W3PLiVIcmE

## Slide 13: Digital Implementation
The difference equations describing a digital PID are typically implemented in a microcontroller or in an FPGA (field-programmable gate array) device.
Pseudocode
Difference equations
previous_error = 0
integral = 0
Start:
error = setpoint – measured_value
proportional = Kp*error
integral = integral + Ki*sampling_time*error
derivative = Kd*(error – previous_error) /sampling_time
output = proporcional + integral + derivative
previous_error = error
wait (samplig_time)
goto Start

## Slide 14: Digital Implementation
PLC (Programmable logic controller) with a digital PID control module
Digital PIDs

## Slide 15: Digital Implementation
What is a PLC? Basics of PLCs
https://www.youtube.com/watch?v=iWgHqqunsyE

## Slide 16: PID Tuning
Manual Tuning
The effects of each of the controller parameters, and on a closed-loop system are summarized in the table below.
PID gains | Closed-Loop Response |  |  | 
 | Rise Time | Overshoot | Settling time | Steady-state error
↑ | Decrease | Increase | Small Change | Decrease
↑ | Decrease | Increase | Increase | Eliminate
 | Small change | Decrease | Decrease | No change
PID gains | Closed-Loop Response |  |  | 
 | Rise Time | Overshoot | Settling time | Steady-state error
 | Decrease | Increase | Small Change | Decrease
 | Decrease | Increase | Increase | Eliminate
 | Small change | Decrease | Decrease | No change
Note: Keep in mind that changing one of the PID gains can change the effect of the other two. For this reason, this table should only be used as a reference when you are determining the values for and .

## Slide 17: PID Tuning
Manual Tuning
One possible way is as follows (the controller is connected to the plant):
Set and equal to 0.
Increase until you observe that the step response is fast enough and the steady-state error is small.
Start adding some integral action in order to get rid of the steady state error. Keep in mind that too much can cause instability.
Add some derivative action in order to quickly react to disturbances and/or dampen the response.

## Slide 18: PID Tuning
Heuristic Methods : Ziegler–Nichols method tuning rule
Set the integral and derivative gains to zero ( )
Increase the proportional gain until the output of the control loop starts oscillating with a constant amplitude. The value of at this point is referred to as ultimate gain ().
Measure the period of the oscillations atthe output of the closed-loop system.
Use and to determine the gains of the PID controller according to the following tuning rule table:

## Slide 19: PID Tuning
Heuristic Methods : Ziegler–Nichols method tuning rule
Control Type |  |  | 
P |  | - | -
PI |  |  | -
PD |  | - | 
PID |  |  | 
Pessen Integral Rule |  |  | 
Some overshoot |  |  | 
No overshoot |  |  | 
Control Type |  |  | 
P |  | - | -
PI |  |  | -
PD |  | - | 
PID |  |  | 
Pessen Integral Rule |  |  | 
Some overshoot |  |  | 
No overshoot |  |  | 
Note: Keep in mind that we are working with heuristic tuning rules, and therefore some additional fine tuning might be necessary.

## Slide 20: PID Tuning
Numerical Optimization Methods
The tuning of a PID controller is posed as a constrained optimization problem.
For a given set of parameters and run a simulation of the closed-loop system, and compute some performance parameters (e.g. setting time, rise time, etc.) and a performance index.
Optimize the performance index over the three PID gains.
Performance Index
Optimizer
PID
Plant Model
Simulation

## Slide 21: PID Tuning
Some Software Tools
Software Tool | Brief Description
pidtool / pidTuner | It is a Matlab tool to interactively design a SISO PID controller in the feed-forward path of single-loop, unity-feedback control configuration.
Pidpy | It is a modular PID control library for python that supports PID auto tuning. https://pypi.python.org/pypi/pypid/
INCA PID Tuner | It is a commercial tuning tool developed by IPCOS. It has a vast library of PID structures for DCS and PLC Systems including Siemens, ABB, Honeywell, Emerson, etc. http://www.ipcos.com/advancedprocesscontrol/advanced-process-control/pid-tuning-software/inca-pid-tuning/

## Slide 22: PID Tuning
pidtool /pidTuner - Demo
https://www.youtube.com/watch?v=2tKe0caUv1I

## Slide 23: PID Tuning
INCA PID Tuner – Demo
https://www.youtube.com/watch?v=XH2bkq1URSg