## Slide 1: An introduction to control
Lecture 14

## Slide 2: What is control?
The goal is to find an input (control signal ) such that process produces the desired output
Open loop control system: the actual output signal has no effect on the control action
Remember the example of pouring a glass of water without looking at the glass

## Slide 3: A general set-up of a closed loop system
We will focus on closed loop control systems
  Example: Inverted pendulum
+
+
-1
Notes: In a closed loop control system the actuating error signal , which is the difference between the input signal (the desired output) and the feedback signal (the actual output), is fed to the controller so as to reduce the error and bring the output of the system to a desired value.
Show example of inverted pendulum. Students can also play with this at home
In a closed loop control system the actuating error signal 𝐸, which is the difference between the input signal 𝑅 (the desired output) and the feedback signal 𝑌 (the actual output), is fed to the controller so as to reduce the error and bring the output of the system 𝑃 to a desired value.
Show example of inverted pendulum. Students can also play with this at home

## Slide 4: But what is C
On-off controller
  Thermostate at home
LTI-System (this course)
  Cruise-control in your car
More advanced controllers exist

## Slide 5: What is good control?
Before we will start to design control systems we will first focus on the question. What is good control?
It depends on the application
  Stability
  Disturbance rejection
  Reference tracking (speed)
  Sensitivity to errors on model
  Etc...

## Slide 6: Examples (stability)
Space shuttles are like inverted pendulums. How do you make sure they don’t flip over.

## Slide 7: Examples: Disturbance rejection
Your body will try to keep the temperature in your body as constant as possible. No matter what the outside temperature is. Two people will have almost the same body temperature.
Jack Zalium
Enduring
https://creativecommons.org/licenses/by-nd/2.0/
Flickr.com
tent86
Marathon Des Sables 046

## Slide 8: Examples: reference tracking
Audi has a system for automatic driving in traffic jams. The audi will follow the car in front of him at an appropriate distance.
https://www.youtube.com/watch?v=Qa_ZSRj0WM0

## Slide 9: Exercise: name the correct property ...

## Slide 10
with
with
The transfer function from and to

## Slide 11: Transfer function from to
We define as the transfer function from to
This transfer function will help us to evaluate tracking
Almost perfect tracking: the output will follow very closely  .

## Slide 12: Transfer function from to
We define as the transfer function from to .
If the disturbance rejection is very good the disturbances will have almost no effect on the output 
(open loop gain) is very large
! a large open loop amplification might lead to an unstable system

## Slide 13: Example: Which controller do you prefer?
The transfer function from to for two different controllers
First controller
Second Controller

## Slide 14: Example: step response of both controllers
First controller
Second Controller
The output when a step is applied to .

## Slide 15: Quality of reference tracking
Look on the step response from to . All the known criteria can help you to decide the quality
  Rise-time
  Settling time
  Steady state error
  Overshoot
  ...
http://www.newport.com/Control-Theory-Terminology/178319/1033/content.aspx

## Slide 16: Quality of reference tracking
Tracking bandwidth: The frequency range for which is close to .
Tracking bandwidth

## Slide 17: Model errors
In practice, transfer function of might be unknown. It is important to know what the effect of the model errors will be. Sensitivity and robustness are key-concepts to evaluate these effects.
Sensitivity
  Quantifies the effect of a small perturbation on the model will be on the output.
Robustness
  This concept refers to bigger changes on the model. A controller is robust if it works properly over a given set of parameters.

## Slide 18: Sensitivity
Sensitivity is a measure for the effect of a (small) disturbance on the model (e.g. variations in the process parameters)
Look at the effect on the system without disturbances ()

## Slide 19: Sensitivity
Now take the relative change due to this disturbance of the model and take the limit for ; this gives the following (measure of the) sensitivity:
Again, a very large looks like a good choice, but again there is a risk for instability!
Note that the sensitivity can be determined for any parameter

## Slide 20: Example 1: robustness
Suppose we want to stabilize the system . We only know that . We propose to use a proportional controller
  The closed loop transfer function becomes
  The controller stabilizes the system if If we choose very large the system will be robust against changes in .

## Slide 21: Example 2: robustness
Suppose we want to stabilize the system with . If we choose the control law this results in the same transfer function.
Again we choose to ensure stability.
But how does the controller perform on the slightly perturbed system ?
The transfer function from to becomes

## Slide 22: Example 2: robustness
The figure on the right plots
For negative the system becomes unstable. The control system is not robust and useless in practical situations. You shouldn’t use control laws which rely on a pole-zero cancellation.
0
-K+a

## Slide 23: Example 3: Robustness of steady-state error
The steady state error is defined as follows:
A very small steady state error (preferably zero) indicates that the controller tracks the reference very well
For the open loop system with a step reference
  So the open loop controller can be free of a steady state error (for a step reference, ) by calibrating the controller such that
   a precise calibration of the DC gain
final value theorem

## Slide 24: Example 3: Steady state error
Closed loop system:
  The steady state error is small if is very large
  Again, calibrating the DC gain
  However, the difference is that here, we only need a large value for it, which is far less demanding than having to make it equal to 1

## Slide 25: An open loop controller is not robust
We can now show how this results in a great advantage of the closed loop strategy over the open loop strategy:
  If changes slightly (for instance due to a factor that has not been taken up into the model) to
  Then making small would require to calibrate anew
  Whereas would remain small, as long as remains large
Hence an open loop controller cannot control the output robustly against changes in

## Slide 26: Type of a system
for a step reference (with size )
So if has at least a pole in zero
For a reference function , we have
So if has at least two poles in zero

## Slide 27: Type of a system
The type of a system is linked to the number of poles has in zero, and hence it is linked to what type of references it can track perfectly
Write as with the amount of poles in zero
Then we say this system is of type
  It will be able to track references of shape up to perfectly (for )
  A reference of shape will be missed by a finite factor (for )
  A reference of shape will be missed by infinity (for )

## Slide 28: Example of a type 0 system
Step reference ()
with the position constant
Ramp reference ()

## Slide 29: Steady state errors – type of a system
With:
  = position constant
  = velocity constant
  = acceleration constant
And the respective steady state errors are, for different system types:
Type | Step | Ramp | Parabole
0 |  |  | 
1 |  |  | 
2 |  |  | 
0 |  |  | 
1 |  |  | 
2 |  |  | 

## Slide 30: Noise rejection and disturbance rejection
Both refer to rejection of the input but are not the same
Measurement noise is often modelled by white noise. (High frequency signal)
Disturbances are actual changes to the state of the system.
+
+
-1

## Slide 31: Noise versus Disturbances
Cruise control
  Measurement errors on the speed are noise
  A change in slope is a disturbance

## Slide 32: Noise versus disturbance
Remember from the start of the lecture
Choosing sufficiently small results in the rejection of D. This can be achieved by choosing sufficiently high.
+
+
-1

## Slide 33: Disturbance versus noise
But what happens to measurement noise
  The amplified measurement noise will be applied to the input of the plant.
  In reality measurement noise requires no control actions. Good noise rejection means that the controller ignores this noise.
+
+
-1

## Slide 34: Disturbance versus noise rejection
Good disturbance rejection requires fast action to bring the state back to the desired state
Good noise rejection requires that measurement noise will be ignored.
Note that a controller can not see the difference between measurement noise and disturbances. Slow controllers will be less sensitive to measurement noise. Fast system will have better disturbance rejection.

## Slide 35: Classical trade-offs in control theory
Slow controllers
  Not sensitive to noise
  Small control inputs
Fast Controllers
  Good disturbance rejection
  Fast tracking
Robust controllers
  Model errors will not affect the behaviour of the system strongly
Aggressive controllers
  exchanges robustness for better performance